## Slide 1: ACS6300 Robotics Project and Dissertation Topic:- MR Fluid Based Haptic Feedback System by, Samanta Suprio Sujoy Project Code and Title: SD1, Medical Robotics- VR/AR for telerobotics
Supervisor :- Professor Sanja Dogramadzi
Second Reader :- Professor Michael Balikhin

## Slide 2: Outline
Aims and Objectives
Background
Typical Behaviour of MR Fluids
Haptic Feedback System
Methodology
The Silicone Haptic Device
Results from Early Prototypes
Overall System
Results
Conclusion and Future Work

## Slide 3: Aims and Objectives
Aim:- To design, manufacture, and assess a tactile feedback system that utilizes magnetorheological fluid to generate lateral and normal forces.
Objectives
To use the Hagen-Poiseuille law and the Herschel-Bulkley model to explain the fluid behavior.
To engineer a silicon rubber haptic device with intricate internal veins and strategically placed input/output ports to enable precise fluid flow control for a single finger.
To develop a system to control and drive the MR fluid using electromagnets, a peristaltic pump, and an Arduino microcontroller board.
To assess the forces generated by the haptic device using a 6-axis load cell sensor.

## Slide 4: Background
What are Magnetorheological Fluids?
Ferromagnetic particles
Carrier Fluid
Respond to magnetic Field
Chain Formation of particles
Image produced from [1]
[1]Wikipedia Contributors, “Magnetorheological fluid,” Wikipedia, Aug. 13, 2018. https://en.wikipedia.org/wiki/Magnetorheological_fluid

## Slide 5: Typical Behaviour of an MR Fluid
Pre Yielding behaves as Newtonian Fluid.
Hagen-Poiseuille law
Post Yielding behaves as Non-Newtonian Fluid.
Herschel-Bulkley Model
n = 1 corresponds to Newtonian behavior
n < 1 indicates shear-thinning behavior
n > 1 indicates shear-thickening behavior
Image Produced from [1]
[1] O. Ashour, C. A. Rogers, and W. Kordonsky, “Magnetorheological Fluids: Materials, Characterization, and Devices,” Journal of intelligent material systems and structures, vol. 7, no. 2, pp. 123–130, 1996, doi: 10.1177/1045389X9600700201.
Image produced from [2]
[2] A. Perry, “Explicit Pressure Drop Equations for Herschel-Bulkley Fluid Flow in Pipes,” Center for Model-Based Cyber-Physical Product Development, vol. 20, no. 12, pp. 15–15, Feb. 2018, Accessed: Aug. 31, 2023. [Online]. Available: https://wcc.ep.liu.se/index.php/MODPROD/article/view/634/551

## Slide 6: Haptic Feedback Systems
Tactile information through force, vibration or touch.
Sensation of touch, pressure, temperature and texture through tactile receptors.
Two main haptic technology:
kinesthetic feedback
  Force Feedback on ligaments and muscles
  Move with humans and effect large areas of the body
  Active and Resistive device
  TeslaGlove and Omega3
  MR Fluid based smart glove by Nam et.al
Omega 3
Tesla Glove
MR Fluid actuator
Image produced from [1]
Image produced from [2]
Image produced from [3]
[1]“Haptic Glove for Virtual Reality with Force Feedback | TESLAGLOVE,” Teslasuit. https://teslasuit.io/products/teslaglove/
‌
[2]“omega.x,” Force Dimension. https://www.forcedimension.com/products/omega (accessed Aug. 31, 2023).
[3]Yoon Kwon Nam, M. K. Park, and R. Yamane, “Smart glove: hand master using magnetorheological fluid actuators,” Proceedings of SPIE, Dec. 2007, doi: https://doi.org/10.1117/12.783776.

## Slide 7
  Cutaneous feedback
    Provide normal or lateral forces through Vibration, Pressure Electrotactile, Ultrasonic, Thermal
  Samuel et.al [1] developed a 3DOF skin deformation device, which uses a delta mechanism to generate lateral forces.
  Antonia et. al [2] designed a wearable fingertip haptic device that provide cutaneous feedback through inflation and control of a membrane.
  Andualem et.al [3] used the DRV2605 haptic motor drivers to develop vibrotactile cutaneous feedback for a virtual environment.
3-DOF delta mechanism
Pressure based haptic device
Vibration based haptic device
Image produced from [1]
Image produced from [2]
Image produced from [3]
[1]S. B. Schorr and A. M. Okamura, “Three-Dimensional Skin Deformation as Force Substitution: Wearable Device Design and Performance During Haptic Exploration of Virtual Environments,” IEEE Transactions on Haptics, vol. 10, no. 3, pp. 418–430, Jul. 2017, doi: https://doi.org/10.1109/toh.2017.2672969.
[2]A. Tzemanaki, G. A. Al, C. Melhuish, and S. Dogramadzi, “Design of a Wearable Fingertip Haptic Device for Remote Palpation: Characterisation and Interface with a Virtual Environment,” Frontiers in Robotics and AI, vol. 5, Jun. 2018, doi: https://doi.org/10.3389/frobt.2018.00062.
[3]A. T. Maereg, A. Nagar, D. Reid, and E. L. Secco, “Wearable Vibrotactile Haptic Device for Stiffness Discrimination during Virtual Interactions,” Frontiers in Robotics and AI, vol. 4, Sep. 2017, doi: https://doi.org/10.3389/frobt.2017.00042.

## Slide 8: Methodology
Arduino signals the relay, turning them ON or OFF.
Based on the Arduino's signal, the relay closes the circuit supplying power to the peristaltic pump and the electromagnet.
The pump, in the ON state, circulates the fluid around the patch
The electromagnet, turns the fluid into semi-soild, when magnetized.
Reservoir
Arduino Uno
Relays
Power Supply
Peristaltic Pump
Electromagnet
Inlet Pipe
Outlet
Silicone haptic device
Source: author

## Slide 9: The Silicone haptic device
Two layer silicone rubber with internal hollow channels.
Thickness of approximately 1mm.
Inlet and Outlet channel integrated in the layers.
Cast the top layer and the bottom layer separately.
Mold cross-section for the outer layer
Mold cross-section for the inner layer
3D Model of the cast
Side View
Back View
Inlet
Outlet
Source of Images: author

## Slide 10
Results from the early prototypes
Incomplete casts, air bubbles and deformations.
Difficult to extract and assemble.
Inner layer mold
Outer layer mold
Deformed cast
Air bubbles
Source of Images: author

## Slide 11
Final Iteration
The top layer and the bottom layer casted together.
Cast the upper half and the lower half separately.
Use 3d printed pipes which connect the top half to the bottom half and also act as the inlet/outlet pipe for the fluid.
3D printed I/O Pipe
Source of images: author
3D model of the final iteration
Inlet/outlet Port
Two layered silicone skin
Fluid distribution channels
Silicone rubber skin

## Slide 12
Inlet pipe
Outlet Pipe
Bottom layers
Top layers
60mm
40mm
Improved Mold design
Internal Channels
4mm
Index Finger

## Slide 13
Overall System
Arduino Uno
2-channel Relay
Peristaltic Pump
Electromagnet
Haptic device
Inlet
Outlet
Reservoir
Source: author

## Slide 14: Generation of Normal and Shear forces
Normal Forces
Chain Formation of the ferromagnetic particles exerts pressure on the inner wall.
Creates a pulse on the finger
Shear Forces
Fluid turns semi solid as electromagnet is turned ON, exerts pressure on inner wall.
The combination of force from the chain formation and pump.
Finger
Silicone Haptic device
Internal hollow Channels
Electromagnet
Inner wall
Source: author
Source: author
Electromagnet
Haptic Device
Finger

## Slide 15: Results
The forces generated by the haptic device is measured using a 6-axis load cell.
The activation time of the electromagnet is varied and the forces and torque generated are captured.
Haptic device
Electromagnet
Load Cell
+Z
+X
+Y
Source: author

## Slide 16
Keeping the pump OFF, the electromagnet is magnetized and demagnetized with a delay.
The system is evaluated for activation time of 1000 milli second, 600 milli second, and 200 milli second.
The forces produced in the Z direction is measured and evaluated.
Evaluation of Normal force generation

## Slide 17
Activation time:- 1000 milli second
Source: author

## Slide 18
Activation time:- 600 milli second
Source: author

## Slide 19
Activation time:- 200 milli second
Source: author

## Slide 20
The Pump for this test is always ON.
The system is evaluated with for a delay time of 50 milli second.
The forces in Z direction and torque in Y,Z is evaluated.
Evaluation of Shear forces generation
Flow direction
Source: author

## Slide 21
Forces in Z direction
Source: author

## Slide 22
Torque produced in X and Y direction
Source: author

## Slide 23: Conclusion and future work
Conclusion
The normal forces and shear forces are easy to generate but low in magnitude.
It is important to ensure waterproof seals between the silicon rubber skin, the 3D pipes and the inlet/outlet pipes.
The electromagnets provides instant magnetization and demagnetization, however generates heat after a while.
The fluid responds instantly, however, ferroparticles are segregated from the base oil after 24 hrs, if not used.
Future Work
A control mechanism for varying the magnetic intensity.
The design of the silicone haptic device.
An alternative to relays, the modules gets noisy for very quick switching tasks.
A MR Fluid with better stability and homogeneity.